## Slide 1
✦ BAPO
Utilizing Adjustable Socket System for Managing Unstable Residual Limb Edema in a Complex Diabetic Transtibial Amputee: A Clinical Case Report
Mohamad Firas Wahbeh | Ortho Med O&P Centre | Case Report
Introduction
2
Diabetes mellitus is the leading cause of non-traumatic lower limb amputation globally. For trans-tibia amputees (TTA), successful prosthetic rehabilitation is the primary goal, yet this is frequently complicated by significant residual limb volume fluctuation.
In diabetic patients, daily volume changes can exceed 10% due to underlying vascular compromise and metabolic instability. Traditional static sockets cannot accommodate these changes:
Limb swelling → socket too tight → pain, skin irritation, tissue damage
Limb shrinkage → socket too loose → instability, gait deviations, falls
For K2-level ambulatory (limited household ambulation), comfort and consistency of fit are paramount. Even minor discomfort can lead to complete prosthesis rejection, making dynamic volume management critical.
Aim: To evaluate the RevoFit™ adjustable socket system in managing unstable residual limb edema in a complex diabetic TTA patient, assessing functional, pain, and quality of life outcomes.
Method
3
Study Design
Single-subject clinical case report comparing baseline (traditional socket) with post-intervention (RevoFit™ adjustable socket) outcomes after 6 weeks.
Patient Profile
65-year-old male, Right TTA secondary to diabetic complications, K2 functional level (limited household ambulatory)
Prosthetic Intervention
Modified Patellar Tendon Bearing (PTB) socket incorporating the RevoFit™ system a dial-based mechanism allowing immediate circumferential pressure adjustment without socket removal.
Outcome Measures
Daily pain: Visual Analog Scale (VAS, 0–10)
Quality of life: Prosthesis Evaluation Questionnaire (PEQ-QoL, 0–100)
Functional activity: Daily step count (activity tracker)
Stump volume: Daily circumference fluctuation (%)
Results
4
Primary Outcomes (Pre → Post, 6 weeks)
Daily Pain (VAS): 6.5 → 1.2 (↓ 81.5%)
PEQ-QoL Score: 35 → 88 (↑ 151.4%)
Daily Intermittent Steps: ~450 → 900 (↑ 100%)
Daily Stump Fluctuation: 13.0% → 2.5% (↓ 80.8%)
Functional Level
K-Level remained stable at K2, consistent with expected outcomes in complex diabetic patients where the primary goal is comfort and independence within the home environment, not K-level advancement.
Qualitative Outcomes
Eliminated the need for 2-hour daily pre-donning compression wrapping
No skin injuries or ulcerations; improved interface pressure (80–100 kPa)
Increased independence, reduced reliance on crutch, resumed social activities
Table 1. Summary of Key Outcomes
Metric
Pre
Post
Improvement
K-Level
K2
K2
Stable
VAS Pain (0-10)
6.5
1.2
↓ 81.5%
PEQ-QoL (0-100)
35
88
↑ 151.4%
Daily Steps
~450
900
↑ 100%
Circumf. Fluctuation (%)
13.0%
2.5%
↓ 80.8%
Interface Pressure (kPa)
120-180
80-100
Optimal
Discussion
5
The RevoFit™ system effectively addressed the core challenge of 13.0% daily volume fluctuation a magnitude highly disruptive to static socket interface pressure. By enabling patient-controlled circumferential adjustment, the system reduced this fluctuation to a clinically negligible 2.5%, directly driving the observed improvements in pain, function, and quality of life.
A particularly notable finding was the 13.0% average reduction in maximum circumference measurements (Table 3), suggesting that the consistent, patient-controlled compression provided by the RevoFit™ system acted as an effective long-term compression therapy elevating its clinical significance beyond mere accommodation to active therapeutic management of chronic edema.
Maximizing Function within K2 Classification
The 100% increase in daily steps (450 → 900) represents a maximal functional gain within the K2 classification. For this population, the primary therapeutic goal is comfort, safety, and independence in the home environment not K-level advancement. The profound improvement in QoL (35 → 88) underscores that for complex diabetic amputees, prosthetic fit is the primary driver of functional independence.
These results align with published literature (Brzostowski 2019; Baldock 2023) demonstrating that adjustable sockets improve fit and comfort in trans-tibia amputees with volume fluctuations.
Conclusion
6
The RevoFit™ adjustable socket system is a highly effective intervention for K2-level diabetic transtibial amputees with significant, unstable residual limb edema. The system achieved:
81.5% reduction in daily pain (VAS 6.5 → 1.2)
151.4% improvement in quality of life (PEQ-QoL 35 → 88)
100% increase in daily functional steps (450 → 900)
80.8% reduction in daily stump volume fluctuation (13.0% → 2.5%)
By providing patient-controlled volume compensation, this technology maximises independence and prosthetic use, offering a compelling clinical and economic value proposition for this challenging patient population.
References
7
1. Sanders JE, Fatone S. Residual limb volume change: systematic review of measurement and management. J Rehabil Res Dev. 2011;48(8):949-86.
2. Baldock M, et al. Adjustable prosthetic sockets: a systematic review of industrial and research design characteristics. J Neuroeng Rehabil. 2023;20(1):147.
3. Brzostowski JT, et al. Adjustable sockets may improve residual limb fluid volume retention in transtibial prosthesis users. Prosthet Orthot Int. 2019;43(3):250-256.
Keywords: Transtibial Amputation · Diabetes Mellitus · Residual Limb Edema · Adjustable Socket · RevoFit™ · K2 Level · Case Report
BAPO Annual Conference | firaswahbeh76@gmail.com | Ortho Med O&P Centre